Liquid-liquid equilibrium data for quaternary systems with choline chloride and diols: separation of azeotropic mixtures

Liubichev D.A., Samarov A.A., Prikhodko I.V.

1st year PhD student

Saint Petersburg State University, Institute of Chemistry, Saint Petersburg, Russia

E-mail: dmitrylyubichev@gmail.com

Deep eutectic solvents (DES) which are intensively investigated in recent time present especial interest for scientists. They are considered as the way for ‘green chemistry’ future with minimized affection of chemical-based pollutants. DESs can be useful for solving different issues, according to published articles. For instance, some DESs show promise to be CO2 capture with high carbon dioxide solubilities, low vapor pressures and high thermal stabilities [1]. Otherwise, DESs possess several key characteristics that demonstrate great potential to facilitate new biocatalytic pathways [2].  Furthermore, DESs can be used as extractants for separation different mixtures like biodiesel, aromatic hydrocarbons, gas and biologically active compounds [3]. Particularly, DESs are considered as new generation solvents for separation azeotropic mixtures e.g., for purification ester from alcohol in esterification reaction. This way opens the perspectives in using DES for ester-based second-generation biofuels and all-new fuel additives for gasoline [4].

This work is a continuation of the investigation of liquid-liquid equilibria (LLE) of DES formed by choline chloride and dibasic carboxylic acids/glycerol/urea in alcohol-ester systems [5]. In the present paper, we consider the ability of DESs based on choline chloride and diols (ethane-1,2-diol and propane-1,2-diol) for the separation of ethanol, n-propanol, and n-butanol with corresponding acetate esters. Tie-lines were obtained at temperatures 293.15 K and 313.15 K and atmospheric pressure. The compositions of coexisting organic and DES phases are determined by 1H NMR spectroscopy. The extraction performance was characterized with distribution coefficients and values of selectivity for used alcohols. NRTL model was applied to correlate LLE in these systems.

This study was supported by the Russian Science Foundation (grant 19-73-00092). The experimental work was facilitated by the equipment of Magnetic Resonance Research Centre at St. Petersburg State University. Authors are grateful for support for Committee for Science and Higher Education of the Government of St. Petersburg.

References

1. Jenkins R. W. и др. Potential renewable oxygenated biofuels for the aviation and road transport sectors // Fuel. 2013. Т. 103. С. 593–599.

2. Larriba M. и др. Choline Chloride-Based Deep Eutectic Solvents in the Dearomatization of Gasolines // ACS Sustain. Chem. Eng. 2018. Т. 6. № 1. С. 1039–1047.

3. Samarov A. и др. Liquid-liquid equilibrium of alcohol–ester systems with deep eutectic solvent on the base of choline chloride // J. Chem. Thermodyn. 2019a. Т. 131. С. 369–374.

4. Samarov A. и др. Liquid-Liquid Equilibria for Separation of Alcohols from Esters Using Deep Eutectic Solvents Based on Choline Chloride: Experimental Study and Thermodynamic Modeling // J. Chem. Eng. Data. 2019b. Т. 64. № 12. С. 6049–6059.

5. Sarmad S., Mikkola J. P., Ji X. Carbon Dioxide Capture with Ionic Liquids and Deep Eutectic Solvents: A New Generation of Sorbents // ChemSusChem. 2017. Т. 10. № 2. С. 324–352.